Suspension Geometry Program - written by Wm. C. Mitchell

(c) Copyright 1983, 1997 - All rights reserved.

Body/CAD program version 6.00;  January, 1997.

The file name is OUTPUT

*********************************************************

SRF Rear w/4" Ride Height (No Driver, No Body)

Spec Racer Rear Suspension

*********************************************************

Suspension type is 3 using SRF_R97.GEO for Rocker Arm

MacPherson_Type is False

Solid Rear axle type is False

Watts-pivot Type is False

Steering box/drag link type is False

Double Crank (Lola-Indy Car Rear) is False

ROCKER Structure specification:  Double A-Arm with Swaybar

Upper and lower wishbones with a steering tie-rod.

Model supports spring/shock, swaybar and halfshaft but not bellcrank.

Spring/shock and swaybar may be attached to:  Lower wishbone

Upper wishbone (default)

Hub

The steering Tie-rod may be attached to:  Tub, chassis or frame (default)

Lower wishbone

Upper wishbone

Specify Suspension and Attachments:

Steering tie-rod attached to Tub

Do NOT process half-shaft

Spring/Shock absorber attached to Upper

Perform extra Motion Ratio computations (adds processing time).

Anti-roll or stabilizer bar attached to Upper

NO Push/Pull rod:  Spring/Shock absorber operates directly

OUTPUT  SRF Rear w/4" Ride Height

Suspension Points: Both sides symmetric   Fore/Aft       Width    Vertical

Coordinate system origin is at          0.000       0.000       0.000

Lower-inner forward tub mount   A     -18.125      11.500       7.625

Lower ball joint                B       0.250      26.500       7.250

Lower-inner rearward tub mount  C       9.500       8.250       5.000

Upper-inner forward tub mount   D      -0.875      12.875      16.125

Upper ball joint                E       0.250      22.250      17.500

Upper-inner rearward tub mount  F       5.875      12.875      16.438

Steering Arm mount on hub       S       4.875      25.375      10.500

Tub mount for steering arm      T       8.500       9.879       8.688

Wheelbase and Track                    92.000      56.750

Rim Width and Tire Diameter                         8.000      22.000

Initial Camber and Toe settings        -5.500       0.000

Center of Gravity                     -35.750                  12.780

Toe Measure/Steering Rack Travel                    0.000

Tub mount of spring/shock       U       6.625       3.500       5.000

Activation end of spring/shock  V       5.500       4.500      18.313

Roll-bar blade pivot point      X      10.250       6.687      11.188

Roll-bar mount inboard          Y      10.250       0.000      11.188

Roll-bar blade meets drop-link  Z       4.625       6.687      11.188

Roll-bar drop-link attachment   R       4.625       6.687      16.750

Chassis clearance check         L       0.000       0.000       0.000

OUTPUT  SRF Rear w/4" Ride Height

Computed suspension lengths: Both sides

Length of forward Lower link   A-B      23.723

Length of rearward lower link  C-B      20.584

Perpendicular lower link length         16.955

Front View Projection lower length      17.216

Length of forward Upper link   D-E       9.542

Length of rearward upper link  F-E      10.984

Perpendicular upper link length          9.441

Front View Projection upper length       9.468

Distance between ball joints   B-E      11.096

Tie Rod Length                 S-T      16.017

Rollout or tire circumference           69.115

Damper Length                  U-V      13.398

Swaybar Blade length           X-Z       5.625

Swaybar Rod length             Z-R       5.562

Static Caster (in degrees)               0.000

King Pin angle (in degrees)             22.521

King Pin Offset/Scrub Radius            -1.131

Caster Trail                            -0.250

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is  0.000 (Droop or Rebound)     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -5.500    -5.500       0.000     -1.088     -0.005   -0.005  -0.010

1.00     -6.370    -4.687      -2.670     -1.082      0.012   -0.021  -0.009

2.00     -7.300    -3.929      -5.400     -1.065      0.030   -0.036  -0.006

3.00     -8.294    -3.225      -8.240     -1.033      0.049   -0.050  -0.001

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00      0.000     0.000     0.000    0.000   0.000      -82.815     14.512

1.00      0.368    -0.351    -0.026   -0.025   0.001      -86.873     14.592

2.00      0.754    -0.687    -0.053   -0.047   0.005      -91.127     14.648

3.00      1.160    -1.007    -0.080   -0.068   0.012      -95.631     14.682

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00      178.712     -6.845      178.712     -6.845       -1.088     13.868

1.00      280.598    -11.796      132.318     -4.612       -1.082     13.862

2.00      700.344    -32.384      105.517     -3.329       -1.065     13.845

3.00    -1167.555     59.706       87.894     -2.483       -1.033     13.813

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00      0.000     0.000      0.878     0.877     0.771     0.770    -0.000

1.00      0.435    -0.435      0.878     0.878     0.771     0.770     6.453

2.00      0.871    -0.869      0.879     0.878     0.773     0.770    12.927

3.00      1.307    -1.303      0.882     0.878     0.777     0.771    19.445

SRF Rear w/4" Ride Height

Ride Travel is  0.000 (Droop or Rebound)     Steering Rack travel is   0.000

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.878     0.877      0.00%     0.00%     Plunge not done

1.00      0.878     0.878      0.05%     0.06%     Plunge not done

2.00      0.879     0.878      0.30%     0.06%     Plunge not done

3.00      0.882     0.878      0.83%     0.13%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00      0.321     0.321      0.841     0.841

1.00      0.204     0.433      0.899     0.785

2.00      0.082     0.543      0.959     0.730

3.00     -0.049     0.652      1.024     0.676

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00        -0.000

1.00         0.004

2.00         0.007

3.00         0.011

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is  1.000 (Droop or Rebound)     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -5.299    -5.299      -0.000     -0.316      0.020    0.020   0.040

1.00     -6.294    -4.368     -11.362     -0.274      0.041    0.000   0.041

2.00     -7.358    -3.497     -21.362     -0.156      0.064   -0.019   0.046

3.00     -8.499    -2.683     -29.123      0.019      0.088   -0.036   0.053

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00      0.750     0.750    -0.053    0.053   0.107      -74.975     14.244

1.00      1.148     0.370    -0.080    0.026   0.107      -78.693     14.366

2.00      1.567     0.007    -0.108    0.000   0.108      -82.505     14.459

3.00      2.009    -0.340    -0.135   -0.024   0.111      -86.454     14.526

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00      718.836     -8.003      718.836     -8.003       -0.316     14.096

1.00    -1120.998     18.017      283.612     -1.956       -0.274     14.054

2.00     -295.622      6.510      179.970     -0.564       -0.156     13.936

3.00     -162.258      4.771      133.031      0.045        0.019     13.761

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00      0.878     0.878      0.878     0.879     0.772     0.772     0.000

1.00      1.314     0.443      0.881     0.877     0.776     0.770     6.577

2.00      1.752     0.009      0.885     0.877     0.782     0.769    13.199

3.00      2.193    -0.425      0.891     0.877     0.794     0.769    19.914

SRF Rear w/4" Ride Height

Ride Travel is  1.000 (Droop or Rebound)     Steering Rack travel is   0.000

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.878     0.879      0.10%     0.28%     Plunge not done

1.00      0.881     0.877      0.60%     0.00%     Plunge not done

2.00      0.885     0.877      1.49%    -0.07%     Plunge not done

3.00      0.891     0.877      2.95%    -0.06%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00      0.080     0.080      0.960     0.960

1.00     -0.051     0.202      1.025     0.900

2.00     -0.194     0.318      1.096     0.842

3.00     -0.353     0.431      1.176     0.786

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00         0.000

1.00         0.005

2.00         0.009

3.00         0.015

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is -1.000(  1.000 Bump or Jounce)     Steering Rack travel is   0.0

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -5.935    -5.935      -0.000     -1.894     -0.058   -0.058  -0.117

1.00     -6.692    -5.233      -1.412     -1.889     -0.045   -0.071  -0.116

2.00     -7.503    -4.584      -2.872     -1.876     -0.030   -0.083  -0.113

3.00     -8.372    -3.988      -4.432     -1.851     -0.015   -0.093  -0.109

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00     -0.704    -0.704     0.048   -0.048  -0.096      -91.672     14.746

1.00     -0.364    -1.028     0.025   -0.068  -0.093      -96.306     14.794

2.00     -0.007    -1.338     0.001   -0.085  -0.085     -101.267     14.821

3.00      0.367    -1.632    -0.026   -0.097  -0.071     -106.630     14.828

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00      105.050     -7.009      105.050     -7.009       -1.894     13.674

1.00      131.612     -9.214       87.556     -5.555       -1.889     13.669

2.00      177.469    -13.031       75.054     -4.509       -1.876     13.656

3.00      277.642    -21.414       65.601     -3.706       -1.851     13.631

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

-----     --------   ------    --------   ------   --------  ------    ------

0.00     -0.878    -0.878      0.880     0.880     0.774     0.774     0.000

1.00     -0.444    -1.313      0.880     0.878     0.774     0.771     6.435

2.00     -0.009    -1.747      0.879     0.878     0.773     0.771    12.875

3.00      0.427    -2.179      0.880     0.875     0.774     0.766    19.326

SRF Rear w/4" Ride Height

Ride Travel is -1.000(  1.000 Bump or Jounce)     Steering Rack travel is   0.0

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.880     0.880      0.39%     0.53%     Plunge not done

1.00      0.880     0.878      0.43%     0.21%     Plunge not done

2.00      0.879     0.878      0.33%     0.11%     Plunge not done

3.00      0.880     0.875      0.45%    -0.54%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00      0.545     0.545      0.730     0.730

1.00      0.435     0.654      0.784     0.676

2.00      0.323     0.763      0.840     0.622

3.00      0.206     0.873      0.898     0.567

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00        -0.000

1.00         0.003

2.00         0.007

3.00         0.010

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is  2.000 (Droop or Rebound)     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -5.360    -5.360      -0.000      0.371      0.019    0.019   0.038

1.00     -6.501    -4.295      15.430      0.246      0.046   -0.006   0.040

2.00     -7.731    -3.299      39.281     -0.263      0.076   -0.029   0.047

3.00     -9.063    -2.366     106.705     -2.218      0.109   -0.050   0.059

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00      1.550     1.550    -0.108    0.108   0.216      -67.688     13.918

1.00      1.983     1.139    -0.135    0.081   0.216      -71.272     14.095

2.00      2.441     0.747    -0.163    0.054   0.217      -74.854     14.235

3.00      2.928     0.372    -0.192    0.027   0.219      -78.478     14.344

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00     -292.114     -3.813     -292.114     -3.813        0.371     14.409

1.00     -161.225     -0.906    -1071.259    -20.400        0.246     14.534

2.00     -106.488      0.413      741.301     17.804       -0.263     15.043

3.00      -75.917      1.246      287.114      8.121       -2.218     16.998

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00      1.759     1.759      0.885     0.884     0.782     0.782    -0.000

1.00      2.199     1.322      0.891     0.881     0.793     0.776     6.904

2.00      2.643     0.886      0.900     0.879     0.810     0.772    13.898

3.00      3.094     0.452      0.915     0.878     0.837     0.770    21.093

SRF Rear w/4" Ride Height

Ride Travel is  2.000 (Droop or Rebound)     Steering Rack travel is   0.000

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.885     0.884      1.49%     1.52%     Plunge not done

1.00      0.891     0.881      2.88%     0.76%     Plunge not done

2.00      0.900     0.879      5.09%     0.29%     Plunge not done

3.00      0.915     0.878      8.52%     0.08%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00     -0.196    -0.196      1.098     1.098

1.00     -0.355    -0.053      1.177     1.027

2.00     -0.538     0.077      1.268     0.962

3.00     -0.755     0.200      1.375     0.901

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00         0.000

1.00         0.007

2.00         0.014

3.00         0.022

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is -2.000(  2.000 Bump or Jounce)     Steering Rack travel is   0.0

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -6.594    -6.594      -0.000     -2.702     -0.142   -0.142  -0.283

1.00     -7.241    -6.000      -1.046     -2.695     -0.131   -0.151  -0.283

2.00     -7.942    -5.461      -2.128     -2.675     -0.120   -0.160  -0.280

3.00     -8.697    -4.976      -3.282     -2.641     -0.108   -0.166  -0.275

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00     -1.366    -1.366     0.085   -0.085  -0.170     -102.116     14.966

1.00     -1.052    -1.664     0.068   -0.097  -0.166     -107.644     14.986

2.00     -0.723    -1.948     0.048   -0.104  -0.152     -113.687     14.988

3.00     -0.378    -2.217     0.026   -0.105  -0.130     -120.359     14.972

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00       74.769     -7.121       74.769     -7.121       -2.702     13.482

1.00       87.183     -8.596       65.373     -5.994       -2.695     13.475

2.00      104.533    -10.647       57.963     -5.090       -2.675     13.455

3.00      130.828    -13.751       51.933     -4.340       -2.641     13.421

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00     -1.758    -1.758      0.879     0.880     0.773     0.774     0.000

1.00     -1.324    -2.191      0.881     0.878     0.777     0.770     6.458

2.00     -0.889    -2.623      0.881     0.874     0.777     0.764    12.906

3.00     -0.454    -3.052      0.882     0.868     0.778     0.753    19.336

SRF Rear w/4" Ride Height

Ride Travel is -2.000(  2.000 Bump or Jounce)     Steering Rack travel is   0.0

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.879     0.880      0.31%     0.60%     Plunge not done

1.00      0.881     0.878      0.74%     0.07%     Plunge not done

2.00      0.881     0.874      0.76%    -0.81%     Plunge not done

3.00      0.882     0.868      0.89%    -2.16%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00      0.766     0.766      0.622     0.622

1.00      0.657     0.876      0.676     0.567

2.00      0.548     0.988      0.729     0.512

3.00      0.438     1.103      0.784     0.455

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00        -0.000

1.00         0.003

2.00         0.007

3.00         0.011

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is  3.000 (Droop or Rebound)     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -5.735    -5.735       0.000      0.883     -0.004   -0.004  -0.007

1.00     -7.068    -4.505      10.586      0.723      0.033   -0.036  -0.003

2.00     -8.526    -3.362      26.807      0.072      0.075   -0.065   0.009

3.00    -10.145    -2.295      71.380     -2.339      0.123   -0.092   0.031

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00      2.411     2.411    -0.163    0.163   0.327      -60.507     13.491

1.00      2.887     1.962    -0.192    0.136   0.328      -64.176     13.747

2.00      3.396     1.537    -0.224    0.109   0.332      -67.729     13.953

3.00      3.947     1.133    -0.262    0.081   0.343      -71.227     14.117

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00     -105.875     -3.295     -105.875     -3.295        0.883     14.897

1.00      -75.610     -1.401     -159.829     -6.502        0.723     15.057

2.00      -55.863     -0.073     -287.607    -13.852        0.072     15.708

3.00      -41.641      0.975    -1013.441    -54.922       -2.339     18.119

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00      2.650     2.650      0.900     0.901     0.811     0.811     0.000

1.00      3.100     2.207      0.915     0.891     0.837     0.795     7.631

2.00      3.559     1.768      0.936     0.885     0.876     0.784    15.487

3.00      4.033     1.331      0.971     0.882     0.942     0.778    23.896

SRF Rear w/4" Ride Height

Ride Travel is  3.000 (Droop or Rebound)     Steering Rack travel is   0.000

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.900     0.901      5.15%     5.36%     Plunge not done

1.00      0.915     0.891      8.55%     3.21%     Plunge not done

2.00      0.936     0.885     13.64%     1.85%     Plunge not done

3.00      0.971     0.882     22.18%     1.03%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00     -0.541    -0.541      1.269     1.269

1.00     -0.758    -0.358      1.377     1.178

2.00     -1.026    -0.199      1.511     1.099

3.00     -1.376    -0.057      1.685     1.028

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00        -0.000

1.00         0.011

2.00         0.023

3.00         0.039

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Ride Travel is -3.000(  3.000 Bump or Jounce)     Steering Rack travel is   0.0

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Chassis     (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Roll in      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

degrees     Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

0.00     -7.477    -7.477       0.000     -3.485     -0.256   -0.256  -0.512

1.00     -8.014    -6.994      -0.947     -3.476     -0.249   -0.262  -0.511

2.00     -8.606    -6.568      -1.924     -3.447     -0.241   -0.266  -0.507

3.00     -9.251    -6.199      -2.960     -3.398     -0.232   -0.269  -0.501

---- Caster ----    -------- Steer --------     Side View Swing Arm

Chassis       (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Roll in      Left/    Right/     Left/    Right/    Net       Length     Height

degrees     Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

0.00     -1.987    -1.987     0.104   -0.104  -0.208     -114.950     15.182

1.00     -1.700    -2.260     0.097   -0.104  -0.202     -121.843     15.180

2.00     -1.398    -2.518     0.085   -0.097  -0.183     -129.540     15.158

3.00     -1.080    -2.762     0.069   -0.081  -0.150     -138.233     15.118

Chassis       --------- Front View Swing Arm ----------      Roll Center Height

Roll in       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

degrees       Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

0.00       57.742     -7.101       57.742     -7.101       -3.485     13.265

1.00       65.104     -8.257       51.748     -6.145       -3.476     13.256

2.00       74.431     -9.703       46.747     -5.330       -3.447     13.227

3.00       86.740    -11.597       42.494     -4.620       -3.398     13.178

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis     - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Roll in      Left/     Right/     Left/     Right/    Left/    Right/    Twist

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

0.00     -2.637    -2.637      0.877     0.877     0.769     0.769    -0.000

1.00     -2.205    -3.066      0.881     0.871     0.776     0.758     6.460

2.00     -1.772    -3.492      0.884     0.862     0.781     0.743    12.895

3.00     -1.337    -3.912      0.885     0.849     0.783     0.721    19.278

SRF Rear w/4" Ride Height

Ride Travel is -3.000(  3.000 Bump or Jounce)     Steering Rack travel is   0.0

Chassis     - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Roll in      Left/     Right/     Left/     Right/    Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

0.00      0.877     0.877     -0.23%    -0.14%     Plunge not done

1.00      0.881     0.871      0.69%    -1.50%     Plunge not done

2.00      0.884     0.862      1.26%    -3.52%     Plunge not done

3.00      0.885     0.849      1.57%    -6.31%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Chassis     (degrees per inch)   (degrees per deg)

Roll in      Left/     Right/     Left/     Right/

degrees     Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

0.00      0.992     0.992      0.512     0.512

1.00      0.880     1.107      0.567     0.456

2.00      0.770     1.225      0.622     0.398

3.00      0.661     1.348      0.675     0.337

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Chassis         (inches per inch)              (inches per degree)

0.00        -0.000

1.00         0.004

2.00         0.008

3.00         0.012

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Chassis Roll is  0.000 degrees     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Ride       (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Height      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

3.00     -5.735    -5.735       0.000      0.883     -0.004   -0.004  -0.007

2.00     -5.360    -5.360      -0.000      0.371      0.019    0.019   0.038

1.00     -5.299    -5.299      -0.000     -0.316      0.020    0.020   0.040

0.00     -5.500    -5.500       0.000     -1.088     -0.005   -0.005  -0.010

-1.00     -5.935    -5.935      -0.000     -1.894     -0.058   -0.058  -0.117

-2.00     -6.594    -6.594      -0.000     -2.702     -0.142   -0.142  -0.283

-3.00     -7.477    -7.477       0.000     -3.485     -0.256   -0.256  -0.512

---- Caster ----    -------- Steer --------     Side View Swing Arm

Ride         (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Height      Left/    Right/     Left/    Right/    Net       Length     Height

Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

3.00      2.411     2.411    -0.163    0.163   0.327      -60.507     13.491

2.00      1.550     1.550    -0.108    0.108   0.216      -67.688     13.918

1.00      0.750     0.750    -0.053    0.053   0.107      -74.975     14.244

0.00      0.000     0.000     0.000    0.000   0.000      -82.815     14.512

-1.00     -0.704    -0.704     0.048   -0.048  -0.096      -91.672     14.746

-2.00     -1.366    -1.366     0.085   -0.085  -0.170     -102.116     14.966

-3.00     -1.987    -1.987     0.104   -0.104  -0.208     -114.950     15.182

Ride         --------- Front View Swing Arm ----------      Roll Center Height

Height       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

3.00     -105.875     -3.295     -105.875     -3.295        0.883     14.897

2.00     -292.114     -3.813     -292.114     -3.813        0.371     14.409

1.00      718.836     -8.003      718.836     -8.003       -0.316     14.096

0.00      178.712     -6.845      178.712     -6.845       -1.088     13.868

-1.00      105.050     -7.009      105.050     -7.009       -1.894     13.674

-2.00       74.769     -7.121       74.769     -7.121       -2.702     13.482

-3.00       57.742     -7.101       57.742     -7.101       -3.485     13.265

SRF Rear w/4" Ride Height

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis Roll is  0.000 degrees     Steering Rack travel is   0.000

Ride       - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Height      Left/     Right/     Left/     Right/    Left/    Right/    Twist

Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

-----     --------   ------    --------   ------   --------  ------    ------

3.00      2.650     2.650      0.900     0.901     0.811     0.811     0.000

2.00      1.759     1.759      0.885     0.884     0.782     0.782    -0.000

1.00      0.878     0.878      0.878     0.879     0.772     0.772     0.000

0.00      0.000     0.000      0.878     0.877     0.771     0.770    -0.000

-1.00     -0.878    -0.878      0.880     0.880     0.774     0.774     0.000

-2.00     -1.758    -1.758      0.879     0.880     0.773     0.774     0.000

-3.00     -2.637    -2.637      0.877     0.877     0.769     0.769    -0.000

Ride       - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Height      Left/     Right/     Left/     Right/    Left/     Right/

Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

3.00      0.900     0.901      5.15%     5.36%     Plunge not done

2.00      0.885     0.884      1.49%     1.52%     Plunge not done

1.00      0.878     0.879      0.10%     0.28%     Plunge not done

0.00      0.878     0.877      0.00%     0.00%     Plunge not done

-1.00      0.880     0.880      0.39%     0.53%     Plunge not done

-2.00      0.879     0.880      0.31%     0.60%     Plunge not done

-3.00      0.877     0.877     -0.23%    -0.14%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Ride       (degrees per inch)   (degrees per deg)

Height      Left/     Right/     Left/     Right/

Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

3.00     -0.541    -0.541      1.266     1.266

2.00     -0.196    -0.196      1.096     1.096

1.00      0.080     0.080      0.961     0.961

0.00      0.321     0.321      0.842     0.842

-1.00      0.545     0.545      0.732     0.732

-2.00      0.766     0.766      0.623     0.623

-3.00      0.992     0.992      0.512     0.512

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Ride           (inches per inch)              (inches per degree)

3.00        -0.000

2.00         0.000

1.00         0.000

0.00        -0.000

-1.00        -0.000

-2.00        -0.000

-3.00        -0.000

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Chassis Roll is  1.000 degrees     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Ride       (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Height      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

3.00     -7.068    -4.505      10.586      0.723      0.033   -0.036  -0.003

2.00     -6.501    -4.295      15.430      0.246      0.046   -0.006   0.040

1.00     -6.294    -4.368     -11.362     -0.274      0.041    0.000   0.041

0.00     -6.370    -4.687      -2.670     -1.082      0.012   -0.021  -0.009

-1.00     -6.692    -5.233      -1.412     -1.889     -0.045   -0.071  -0.116

-2.00     -7.241    -6.000      -1.046     -2.695     -0.131   -0.151  -0.283

-3.00     -8.014    -6.994      -0.947     -3.476     -0.249   -0.262  -0.511

---- Caster ----    -------- Steer --------     Side View Swing Arm

Ride         (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Height      Left/    Right/     Left/    Right/    Net       Length     Height

Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

3.00      2.887     1.962    -0.192    0.136   0.328      -64.176     13.747

2.00      1.983     1.139    -0.135    0.081   0.216      -71.272     14.095

1.00      1.148     0.370    -0.080    0.026   0.107      -78.693     14.366

0.00      0.368    -0.351    -0.026   -0.025   0.001      -86.873     14.592

-1.00     -0.364    -1.028     0.025   -0.068  -0.093      -96.306     14.794

-2.00     -1.052    -1.664     0.068   -0.097  -0.166     -107.644     14.986

-3.00     -1.700    -2.260     0.097   -0.104  -0.202     -121.843     15.180

Ride         --------- Front View Swing Arm ----------      Roll Center Height

Height       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

3.00      -75.610     -1.401     -159.829     -6.502        0.723     15.057

2.00     -161.225     -0.906    -1071.259    -20.400        0.246     14.534

1.00    -1120.998     18.017      283.612     -1.956       -0.274     14.054

0.00      280.598    -11.796      132.318     -4.612       -1.082     13.862

-1.00      131.612     -9.214       87.556     -5.555       -1.889     13.669

-2.00       87.183     -8.596       65.373     -5.994       -2.695     13.475

-3.00       65.104     -8.257       51.748     -6.145       -3.476     13.256

SRF Rear w/4" Ride Height

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis Roll is  1.000 degrees     Steering Rack travel is   0.000

Ride       - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Height      Left/     Right/     Left/     Right/    Left/    Right/    Twist

Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

-----     --------   ------    --------   ------   --------  ------    ------

3.00      3.100     2.207      0.915     0.891     0.837     0.795     7.631

2.00      2.199     1.322      0.891     0.881     0.793     0.776     6.904

1.00      1.314     0.443      0.881     0.877     0.776     0.770     6.577

0.00      0.435    -0.435      0.878     0.878     0.771     0.770     6.453

-1.00     -0.444    -1.313      0.880     0.878     0.774     0.771     6.435

-2.00     -1.324    -2.191      0.881     0.878     0.777     0.770     6.458

-3.00     -2.205    -3.066      0.881     0.871     0.776     0.758     6.460

Ride       - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Height      Left/     Right/     Left/     Right/    Left/     Right/

Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

3.00      0.915     0.891      8.55%     3.21%     Plunge not done

2.00      0.891     0.881      2.88%     0.76%     Plunge not done

1.00      0.881     0.877      0.60%     0.00%     Plunge not done

0.00      0.878     0.878      0.05%     0.06%     Plunge not done

-1.00      0.880     0.878      0.43%     0.21%     Plunge not done

-2.00      0.881     0.878      0.74%     0.07%     Plunge not done

-3.00      0.881     0.871      0.69%    -1.50%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Ride       (degrees per inch)   (degrees per deg)

Height      Left/     Right/     Left/     Right/

Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

3.00     -0.758    -0.358      1.373     1.176

2.00     -0.355    -0.053      1.175     1.026

1.00     -0.051     0.202      1.025     0.901

0.00      0.204     0.433      0.900     0.787

-1.00      0.435     0.654      0.786     0.678

-2.00      0.657     0.876      0.677     0.569

-3.00      0.880     1.107      0.567     0.456

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Ride           (inches per inch)              (inches per degree)

3.00         0.011

2.00         0.007

1.00         0.005

0.00         0.004

-1.00         0.003

-2.00         0.003

-3.00         0.004

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Chassis Roll is  2.000 degrees     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Ride       (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Height      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

3.00     -8.526    -3.362      26.807      0.072      0.075   -0.065   0.009

2.00     -7.731    -3.299      39.281     -0.263      0.076   -0.029   0.047

1.00     -7.358    -3.497     -21.362     -0.156      0.064   -0.019   0.046

0.00     -7.300    -3.929      -5.400     -1.065      0.030   -0.036  -0.006

-1.00     -7.503    -4.584      -2.872     -1.876     -0.030   -0.083  -0.113

-2.00     -7.942    -5.461      -2.128     -2.675     -0.120   -0.160  -0.280

-3.00     -8.606    -6.568      -1.924     -3.447     -0.241   -0.266  -0.507

---- Caster ----    -------- Steer --------     Side View Swing Arm

Ride         (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Height      Left/    Right/     Left/    Right/    Net       Length     Height

Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

3.00      3.396     1.537    -0.224    0.109   0.332      -67.729     13.953

2.00      2.441     0.747    -0.163    0.054   0.217      -74.854     14.235

1.00      1.567     0.007    -0.108    0.000   0.108      -82.505     14.459

0.00      0.754    -0.687    -0.053   -0.047   0.005      -91.127     14.648

-1.00     -0.007    -1.338     0.001   -0.085  -0.085     -101.267     14.821

-2.00     -0.723    -1.948     0.048   -0.104  -0.152     -113.687     14.988

-3.00     -1.398    -2.518     0.085   -0.097  -0.183     -129.540     15.158

Ride         --------- Front View Swing Arm ----------      Roll Center Height

Height       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

3.00      -55.863     -0.073     -287.607    -13.852        0.072     15.708

2.00     -106.488      0.413      741.301     17.804       -0.263     15.043

1.00     -295.622      6.510      179.970     -0.564       -0.156     13.936

0.00      700.344    -32.384      105.517     -3.329       -1.065     13.845

-1.00      177.469    -13.031       75.054     -4.509       -1.876     13.656

-2.00      104.533    -10.647       57.963     -5.090       -2.675     13.455

-3.00       74.431     -9.703       46.747     -5.330       -3.447     13.227

SRF Rear w/4" Ride Height

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis Roll is  2.000 degrees     Steering Rack travel is   0.000

Ride       - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Height      Left/     Right/     Left/     Right/    Left/    Right/    Twist

Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

3.00      3.559     1.768      0.936     0.885     0.876     0.784    15.487

2.00      2.643     0.886      0.900     0.879     0.810     0.772    13.898

1.00      1.752     0.009      0.885     0.877     0.782     0.769    13.199

0.00      0.871    -0.869      0.879     0.878     0.773     0.770    12.927

-1.00     -0.009    -1.747      0.879     0.878     0.773     0.771    12.875

-2.00     -0.889    -2.623      0.881     0.874     0.777     0.764    12.906

-3.00     -1.772    -3.492      0.884     0.862     0.781     0.743    12.895

Ride       - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Height      Left/     Right/     Left/     Right/    Left/     Right/

Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

3.00      0.936     0.885     13.64%     1.85%     Plunge not done

2.00      0.900     0.879      5.09%     0.29%     Plunge not done

1.00      0.885     0.877      1.49%    -0.07%     Plunge not done

0.00      0.879     0.878      0.30%     0.06%     Plunge not done

-1.00      0.879     0.878      0.33%     0.11%     Plunge not done

-2.00      0.881     0.874      0.76%    -0.81%     Plunge not done

-3.00      0.884     0.862      1.26%    -3.52%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Ride       (degrees per inch)   (degrees per deg)

Height      Left/     Right/     Left/     Right/

Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

3.00     -1.026    -0.199      1.504     1.098

2.00     -0.538     0.077      1.264     0.962

1.00     -0.194     0.318      1.095     0.844

0.00      0.082     0.543      0.960     0.733

-1.00      0.323     0.763      0.841     0.625

-2.00      0.548     0.988      0.731     0.514

-3.00      0.770     1.225      0.622     0.398

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Ride           (inches per inch)              (inches per degree)

3.00         0.023

2.00         0.014

1.00         0.009

0.00         0.007

-1.00         0.007

-2.00         0.007

-3.00         0.008

SRF Rear w/4" Ride Height

Fundamental Analysis of Camber, Steer, Scrub and Roll Center

Chassis Roll is  3.000 degrees     Steering Rack travel is   0.000

---- Camber ----    --- Roll Center ---     ----- Tire Scrub -----

(in degrees)          (in inches)          (measured in inches)

Ride       (Pos. leans out)    (Pos. Horiz Loaded)      (Pos. is wide track)

Height      Left/    Right/    Horizontal Vertical      Left/    Right/   Net

Unloaded  Loaded    Position   Position     Unloaded  Loaded  Scrub

------     --------  ------    --------   --------     --------  -----   -----

3.00    -10.145    -2.295      71.380     -2.339      0.123   -0.092   0.031

2.00     -9.063    -2.366     106.705     -2.218      0.109   -0.050   0.059

1.00     -8.499    -2.683     -29.123      0.019      0.088   -0.036   0.053

0.00     -8.294    -3.225      -8.240     -1.033      0.049   -0.050  -0.001

-1.00     -8.372    -3.988      -4.432     -1.851     -0.015   -0.093  -0.109

-2.00     -8.697    -4.976      -3.282     -2.641     -0.108   -0.166  -0.275

-3.00     -9.251    -6.199      -2.960     -3.398     -0.232   -0.269  -0.501

---- Caster ----    -------- Steer --------     Side View Swing Arm

Ride         (in degrees)       (inch Pos. is left)      (Anti-dive, squat)

Height      Left/    Right/     Left/    Right/    Net       Length     Height

Unloaded  Loaded    Unloaded  Loaded Toe-In       of Arm     of IC

------     --------  ------    --------  -----  ------       ------     ------

3.00      3.947     1.133    -0.262    0.081   0.343      -71.227     14.117

2.00      2.928     0.372    -0.192    0.027   0.219      -78.478     14.344

1.00      2.009    -0.340    -0.135   -0.024   0.111      -86.454     14.526

0.00      1.160    -1.007    -0.080   -0.068   0.012      -95.631     14.682

-1.00      0.367    -1.632    -0.026   -0.097  -0.071     -106.630     14.828

-2.00     -0.378    -2.217     0.026   -0.105  -0.130     -120.359     14.972

-3.00     -1.080    -2.762     0.069   -0.081  -0.150     -138.233     15.118

Ride         --------- Front View Swing Arm ----------      Roll Center Height

Height       Left/Unloaded Side      Right/Loaded Side      Absolute  Relative

Length     Height       Length     Height      to ground  to C.G.

------       ------     ------       ------     ------       ------     ------

3.00      -41.641      0.975    -1013.441    -54.922       -2.339     18.119

2.00      -75.917      1.246      287.114      8.121       -2.218     16.998

1.00     -162.258      4.771      133.031      0.045        0.019     13.761

0.00    -1167.555     59.706       87.894     -2.483       -1.033     13.813

-1.00      277.642    -21.414       65.601     -3.706       -1.851     13.631

-2.00      130.828    -13.751       51.933     -4.340       -2.641     13.421

-3.00       86.740    -11.597       42.494     -4.620       -3.398     13.178

SRF Rear w/4" Ride Height

Spring Travel, Motion Ratio (or Velocity Ratio) and Swaybar Twist

Chassis Roll is  3.000 degrees     Steering Rack travel is   0.000

Ride       - Spring Travel -    - Motion Ratio --   -Ratio Squared--   Swaybar

Height      Left/     Right/     Left/     Right/    Left/    Right/    Twist

Unloaded   Loaded    Unloaded   Loaded   Unloaded  Loaded   degrees

------     --------   ------    --------   ------   --------  ------    ------

3.00      4.033     1.331      0.971     0.882     0.942     0.778    23.896

2.00      3.094     0.452      0.915     0.878     0.837     0.770    21.093

1.00      2.193    -0.425      0.891     0.877     0.794     0.769    19.914

0.00      1.307    -1.303      0.882     0.878     0.777     0.771    19.445

-1.00      0.427    -2.179      0.880     0.875     0.774     0.766    19.326

-2.00     -0.454    -3.052      0.882     0.868     0.778     0.753    19.336

-3.00     -1.337    -3.912      0.885     0.849     0.783     0.721    19.278

Ride       - Motion Ratio --    -- Rising Rate --   Halfshaft Plunge

Height      Left/     Right/     Left/     Right/    Left/     Right/

Unloaded   Loaded    Unloaded   Loaded   Unloaded   Loaded

------     --------   ------    --------   ------   --------   ------

3.00      0.971     0.882     22.18%     1.03%     Plunge not done

2.00      0.915     0.878      8.52%     0.08%     Plunge not done

1.00      0.891     0.877      2.95%    -0.06%     Plunge not done

0.00      0.882     0.878      0.83%     0.13%     Plunge not done

-1.00      0.880     0.875      0.45%    -0.54%     Plunge not done

-2.00      0.882     0.868      0.89%    -2.16%     Plunge not done

-3.00      0.885     0.849      1.57%    -6.31%     Plunge not done

-- Ride Camber --    -- Roll Camber --

Ride       (degrees per inch)   (degrees per deg)

Height      Left/     Right/     Left/     Right/

Unloaded   Loaded    Unloaded   Loaded

------     --------   ------    --------   ------

3.00     -1.376    -0.057      1.676     1.028

2.00     -0.755     0.200      1.371     0.902

1.00     -0.353     0.431      1.174     0.788

0.00     -0.049     0.652      1.024     0.680

-1.00      0.206     0.873      0.899     0.571

-2.00      0.438     1.103      0.785     0.458

-3.00      0.661     1.348      0.675     0.337

Theoretical Analysis of Changes based on Instant Centers

------- Ride Scrub -------      ------- Roll Scrub -------

Ride           (inches per inch)              (inches per degree)

3.00         0.038

2.00         0.022

1.00         0.015

0.00         0.011

-1.00         0.010

-2.00         0.011

-3.00         0.012